## Slide 1: SyR-e: an Open-Souce Tool for Electrical Machines Design
Simone Ferrari
simone.ferrari@polito.it
Dept. of Energy "Galileo Ferraris" – Politecnico di Torino

## Slide 2: Content
  What is SyR-e?
  SyR-e features
  Preliminary Automatic Design
  Design Optimization
  FEA Evaluation/Validation
  Case Study

## Slide 3: What is SyR-e?
SyR-e (Synchronous Reluctance – evolution) is an open-source (*) tool for SyR, PM-SyR and SPM machine design
  Born in 2009 from a collaboration between Politecnico di Torino and Politecnico di Bari, for:
    Investigate SyR geometries with no prejudice of the existing literature
    Provide an automatic design tool for non-expert designers
  In the latest versions, also PM machines are included, as PM-assisted SyR machines, SPM and IPM machines
  Runs in Matlab/Octave
  Uses FEMM for the FEA evaluations
  Graphical User Interface helps to facilitate the design process and the user experience
(*) LICENSE: The C++ programs based on the original FEMM source code are licensed under the Aladdin Free Public License, as the original FEMM source is also provided under this license. The Matlab/Octave code is provided under the Apache Version 2.0 license. Further details and the texts of these licenses are provided with the source.

## Slide 4: Content
  What is SyR-e?
  SyR-e features
  Preliminary Automatic Design
  Design Optimization
  FEA Evaluation/Validation
  Case Study

## Slide 5: SyR-e sections
Manual input of the machine data
Automatic preliminary design
Design Optimization
FEA Evaluation/Validation
Main machine parameters

## Slide 6: Main inputs and rotor geometries
Circular
Iseg
Seg
Fluid
SPM
Vtype

## Slide 7: Stator Parameter

## Slide 8: Rotor Parameter – SyR and PM-SyR
dx=[-1 -1 -1]
dx=[0 0 0]
dx=[+1 +1 +1]
PMs amount in the flux barriers [pu] (Circular only)
Flux Barrier Shift (Circular and Seg)
Structural ribs

## Slide 9: Flux Barrier Shift
Flux Barrier Shift (*) is used to reduce the torque ripple in SyR and PM-SyR machines
  Feature introduced on May 2018
  Available only for Circular and Seg geometries
  On the electrical period, one pole is narrowed by the shift angle, while the other is widened by the same quantity
(*) S. Ferrari, G. Pellegrino, M. Davoli and C. Bianchini, “Reduction of Torque Ripple in Synchronous Reluctance Machines through Flux Barrier Shift”, 2018 XXIII International Conference on Electrical Machines (ICEM), Alexandroupoli, Greece, September 3-6, 2018.
Regular rotor
Shifted rotor

## Slide 10: Mechanical model
Radial ribs allow high-speed operations. SyR-e has two ways to set the radial ribs width:
  Manual setting: manual input of the ribs for each flux barriers (enabled with the correct tick)
  Automatic size: based on a simplified mechanical model (*): each ribs is evaluated as
  For Seg geometry only, is possible to add two ribs per layer (suitable for PM-SyR machines)
(*) M. Palmieri, M. Perta, F. Cupertino and G. Pellegrino, "High-speed scalability of synchronous reluctance machines considering different lamination materials," IECON 2014 - 40th Annual Conference of the IEEE Industrial Electronics Society, Dallas, TX, 2014, pp. 614-620.

## Slide 11: Rotor Parameter – SPM
(*) C. Lu, S. Ferrari, G. Pellegrino, C. Bianchini and M. Davoli, "Parametric design method for SPM machines including rounded PM shape," 2017 IEEE Energy Conversion Congress and Exposition (ECCE), Cincinnati, OH, 2017, pp. 4309-4315.

## Slide 12: Rotor Parameter – Vtype
Structural ribs

## Slide 13: Additional inputs
Thermal model inputs
Thermal model outputs
PM design (Seg)
Maximum speed
Mesh size in FEMM
Mechanical constraints

## Slide 14: Windings setting
Main winding parameters
Winding scheme, computed with koil_syre (*)
(*) koil_syre is a Matlab executable version of Koil (http://koil.sourceforge.net/)
Side-by-side layers (CW)
Number of slots in the FEMM model
Number of three-phase sets (for multiphase machines)

## Slide 15: Material library
Machine groups
Material library, divided in 3 sections.
Is possible to add/remove custom material and view the properties of an existing material

## Slide 16: Content
  What is SyR-e?
  SyR-e features
  Preliminary Automatic Design
  Design Optimization
  FEA Evaluation/Validation
  Case Study

## Slide 17: Preliminary Design
Starting from:
  Machine dimensions (R,l,g)
  The number of poles, stator slots
  The target flux density in the iron
  The maximum allowed copper loss
And using two dimensionless parameters
  ,
The performance figures (T, PF) computed with a pure analytical model are plotted on the parametric design plane

## Slide 18: FEA-Augmented Model (FEAfix)
(*) S. Ferrari and G. Pellegrino, “FEA-Augmented Design Equations for Synchronous Reluctance Machines," 2018 IEEE Energy Conversion Congress and Exposition (ECCE), Portland, OR, September, 23-27 2018.
  FEA simulations of selected point on the design plane to correct the performance figure estimation
  Slower and more precise than the pure analytical model
  Parallel computing enabled for 4+ FEA
  Selection of the number of points for FEA simulations:
  1: center
  4: corners
  5: center + corners
  1000: whole design domain (for debug only)

## Slide 19: Content
  What is SyR-e?
  SyR-e features
  Preliminary Automatic Design
  Design Optimization
  FEA Evaluation/Validation
  Case Study

## Slide 20: Design Optimization
  SyR-e uses Multi-Objective Differential Evolution (MODE) algorithm to perform the design optimization
  The candidate evaluation is performed in with FEA
  Parallel computing enabled under MATLAB environment
Draw the candidate
Call FEMM
MODE
Selection
Mutation
Crossover
Fitness Evaluation

## Slide 21: Multi-Objective Design Optimization
MODE settings
Optimization variables
Optimization objectives

## Slide 22: Content
  What is SyR-e?
  SyR-e features
  Preliminary Automatic Design
  Design Optimization
  FEA Evaluation/Validation
  Case Study

## Slide 23: FEA simulations
Iron loss computation with static FEA (work in progress)
FEA simulation inputs
Current angle in the dq frame.
If 1000: id-iq map

## Slide 24: Content
  What is SyR-e?
  SyR-e features
  Preliminary automatic design
  Design Optimization
  FEA Evaluation/Validation
  Case Study

## Slide 25: Case study
Objective:
Design a SyR rotor for an Induction Machine (IM) stator
Design steps:
  Preliminary design
  FEA post-processing
  Flux Barrier Shift
  Design Optimization
  Design comparison

## Slide 26: Design inputs
The main data of the baseline stator are (*):
  Outer radius = 87,5 mm
  Stack length = 110 mm
  Number of pole pairs = 3
  Number of stator slots = 36
  Winding: single layer, 108 turns in series per phase,
  Iron Material: M600-50A
In addition, some useful data from the baseline machine are:
  Airgap length = 0,325 mm
  Rated copper loss = 170 W
(*) C. Bianchini, M. Davoli, G. Pellegrino, F. Immovilli and E. Lorenzani, "Low cost PM synchronous servo-applications employing asynchronous-motor frame," 2015 IEEE Energy Conversion Congress and Exposition (ECCE), Montreal, QC, 2015, pp. 6090-6095.

## Slide 27: Content
  What is SyR-e?
  SyR-e features
  Preliminary automatic design
  Design Optimization
  FEA Evaluation/Validation
  Case Study
    Preliminary design
    FEA post-processing
    Flux Barrier Shift
    Design optimization
    Design comparison

## Slide 28: Preliminary design – analytical model

## Slide 29: Preliminary design – FEAfix

## Slide 30: Preliminary design – FEA validation

## Slide 31: Content
  What is SyR-e?
  SyR-e features
  Preliminary automatic design
  Design Optimization
  FEA Evaluation/Validation
  Case Study
    Preliminary design
    FEA post-processing
    Flux Barrier Shift
    Design optimization
    Design comparison

## Slide 32: FEA post-processing – single point

## Slide 33: FEA post-processing – magnetic model

## Slide 34: Magnetic model manipulation
Once the machine magnetic model is available, there are some functions (out of the GUI) for the manipulation of the data. They are:
  C_MMLut.m
  C_MtpaMtpvLut.m
  C_torqueVSgamma.m
  C_OperatingLimits.m
  MaxTw.m

## Slide 35: Content
  What is SyR-e?
  SyR-e features
  Preliminary automatic design
  Design Optimization
  FEA Evaluation/Validation
  Case Study
    Preliminary design
    FEA post-processing
    Flux Barrier Shift
    Design optimization
    Design comparison

## Slide 36: Flux Barrier Shift

## Slide 37: Content
  What is SyR-e?
  SyR-e features
  Preliminary automatic design
  Design Optimization
  FEA Evaluation/Validation
  Case Study
    Preliminary design
    FEA post-processing
    Flux Barrier Shift
    Design optimization
    Design comparison

## Slide 38: Design Optimization

## Slide 39: Design Optimization
Evolution
Evolution results
Pareto front re-evaluation (fine)

## Slide 40: Content
  What is SyR-e?
  SyR-e features
  Preliminary automatic design
  Design Optimization
  FEA Evaluation/Validation
  Case Study
    Preliminary design
    FEA post-processing
    Flux Barrier Shift
    Design optimization
    Design comparison

## Slide 41: Design Comparison – MTPA
Preliminary Design
FBS Design
MODE Design

## Slide 42: Design Comparison – Torque waveform
Preliminary Design
FBS Design
MODE Design

## Slide 43: Design Comparison – Torque ripple map
Preliminary Design
FBS Design
MODE Design